## Slide 1: BCT 2305: Data Communication
Data Transmission

## Slide 2: Areas of Analog Application
Old telephone networks
Most television broadcasting at present
Radio broadcasting

## Slide 3: Analog Signals: The Basics
Cycle
Time
Signal
Amplitude
Frequency = Cycles/Second
A typical
sine wave

## Slide 4: Amplitude and Cycle
Amplitude
  Distance above reference line
Cycle
  One complete wave

## Slide 5: Frequency
Frequency
  Cycles per second
  Hertz is the unit used for expressing frequency
Frequency spectrum
  Defines the bandwidth for different analog communication technologies

## Slide 6: Information Representation Using Analog Signals
Information can be represented using analog signals
Analog signals cannot be manipulated easily
Analog signals must be digitized for computer processing
  They must also be presented in binary form for computer processing

## Slide 7: Analog to Digital Conversion
1 0 1 1 0 1 0 0
A to D Converters, Digital Signal Processors (DSP) etc.

## Slide 8: Data Transmission Using Analog Technology
Digital
0s and 1s
Analog
0s and 1s
Digital-to-Analog Modulation and vice versa
Computer
Modem

## Slide 9: Voice Transmission Example
Voice
Carrier Wave
AM Radio Transmission
Analog-to-Analog Modulation

## Slide 10: Frequency Spectrum Defined
Available range of frequencies for communication
Starts from low frequency communication such as voice and progresses to high frequency communication such as satellite communication
The spectrum spans the entire bandwidth of communicable frequencies

## Slide 11: Frequency Spectrum
Low Frequency
High Frequency
Radio
Frequency
Coaxial
Cable
MHz
Satellite
Transmission
Microwave
MHz
Voice
KHz

## Slide 12: Frequency Spectrum
Low-end
  Voice band
Middle
  Microwave
High-end
  Satellite communication

## Slide 13: Bandwidth Definition
Bandwidth, in general, represents a range of frequencies
300 MHz
700 MHz
Bandwidth is 400 MHz

## Slide 14: Usage of the Term Bandwidth
To specify the communication capacity
  A medium such as a coaxial cable is associated with a bandwidth
To indicate the bandwidth of a technology
  Voice grade circuits have a bandwidth of 4 KHz (0-4000 Hz)

## Slide 15: Digitization Consideration
Sample at twice the rate of bandwidth for acceptable quality digitization of voice( Nynguist theorem)
  Sampling rate for voice transmission is there 8000 Hz
So if each sample is represented by 8-bits, the bandwidth required for transmission is 64000 bps – Approximately 64K bps

## Slide 16: Communication Capacity
Bandwidth is indicative of the communication capacity
Communication speed is proportional to bandwidth
  Shannon's law
Units used to represent bandwidth are Hz, bps etc.

## Slide 17: Coaxial Cable Example
Bandwidth of 300 MHz
Comparison with twisted pair
  Higher bandwidth
  Supports faster communication speeds

## Slide 18: Limiting Factors on Communication Speed
Communication Speed
Bandwidth
Technology

## Slide 19: Impact of bandwidth and Technology on Communication Speed
Bandwidth limitation
  Use better technology such as data compression used in modems to increase speed of communication
Bandwidth and technology limitation
  Move to higher bandwidth media such as fiber cables

## Slide 20: Digital Technology-Areas of Application
Computers
New telephone networks
Phased introduction of digital television technology

## Slide 21: Digital Technology
Basics
  Digital signals that could be assigned digital values
Digital computer technology
  Digital signals
  Binary representation
    Encoded into ones and zeros

## Slide 22: Digital Advantage
Processing using computer technology
Programmable services
Better quality due to being able to reconstruct exact digital patterns at the receiving end
Faster communication speeds are possible

## Slide 23: Digital Signal
1 0 1 1 0 1 0 0
Pulse
Time
Signal Strength
Pulse Duration

## Slide 24: The Need for Conversion
Analog-to-Digital Conversation
  Connection of a computer to an analog communication line
Digital-to-Digital Interface
  Connection of a computer to a digital ISDN line
  Connection of different networks using a router

## Slide 25: Digital-to-Analog Interface
Comp.
Sys. 1
Comp.
Sys. 2
Modem
Modem
Digital
Serial
RS-232C
Digital
Serial
RS-232C
Analog
ITU V.90
POTS

## Slide 26: Digital-to-Digital Interface
Comp.
Sys. 1
Comp.
Sys. 2
DSL
Router
DSL
Router
Digital
IEEE 802.3
Digital
IEEE 802.3
Digital Internet

## Slide 27: Digital to Digital Interface
Network 2
Network 1
Router

## Slide 28: Digital to Digital Interface
In general, in digital to digital interface, protocol conversion takes place
  Example: Connecting an Ethernet network to a campus backbone network using a router

## Slide 29: Digitization of Information
Information need to be digitized for computer processing and the transmission of information

## Slide 30: Components of Information
Alphanumeric data
Image
Audio
Video

## Slide 31: Digital Information Processing
Data
Audio
Image
Video
Digitized and Encoded
Digital
Transmission

## Slide 32: The Advantages of Digitization
Information can be processed by the computer
Easy transmission of information over the Internet and other computer networks
Minimize loss of quality during transmission

## Slide 33: Digitization of information
Digitization Of Alphanumeric Data

## Slide 34: The Basis
Alphanumeric data is digitized using well established coding systems

## Slide 35: Codes Used in the Digitization Of Data
Coding Standards
  ASCII
  EBCDIC
  Unicode
ASCII Code example
  A=1000001

## Slide 36: The Unicode
Replaced the ASCII coding system in microcomputers
All variations of the Latin language
  English
  European languages
Chinese and Japanese
18 Major languages
  Eg: Tamil

## Slide 37: Unicode Possibilities
It is a 16-bit code as opposed to the ASCII code that is basically an 8-bit code
It is therefore possible to have 65,536 variations in UNICODE

## Slide 38: Communication With ASCII And EBCDIC
Latin languages can be transmitted in coded form
Other languages
  Bit-mapped image transmission
  Requires considerably more bandwidth
  An exception is the use of true-type fonts to display the characters of a language not supported by ASCII

## Slide 39: Communication With Unicode
Binary encoded transmission
  Latin languages
  18 major languages
  Chinese, Japanese etc.
Transmission itself requires less bandwidth
Universal usability of software in all the supported languages

## Slide 40: Unicode Advantage in WWW Transmissions
Client
Tamil
Web
Site
Internet Explorer
Browser retrieving
Tamil pages on a client supporting Unicode.
Tamil pages are transmitted in their binary encoded form.
Site created using all
the tools such as the
MS-IIS.

## Slide 41: UNICODE Usage
Currently all the computers support UNICODE
Also, the operating systems and the applications also support UNICODE
Both hardware and software support is necessary for the successful implementation of UNICODE

## Slide 42: Digitization Of Audio: Overview
Take samples of audio at pre-determined time intervals known as the sampling rate
Represent the sampled audio with digital signals..Encoding
  Pulse Amplitude Modulation (PAM)
Encode signals into binary code
  Pulse Code Modulation (PCM) that incorporates PAM as well
  Required for computer processing

## Slide 43: Digitization of Audio: Pulse Amplitude Modulation (PAM)
Audio
9 8 7 6 7 9
Digital Signals must further be encoded into binary signals for computer processing and transmission.
Sampling Interval

## Slide 44: Digitization and Encoding of Audio: Pulse Code Modulation (PCM)
PCM is a two step process
First the audio is sampled and represented by digital signals
The digital signals are then encoded in binary form

## Slide 45: Binary Encoding of Signals in Pulse Code Modulation (PCM)
9 8 7 6 5 6
1001 1000 0111 0110 0101 0110
The integer numbers have effectively been coded into zeros and ones. The ones and zeros now contain the audio information encoded in a form that could be processed by a computer.
PCM

## Slide 46: Salient Points on the Digitization Of Audio
Sampling rate and the number of bits used for representing the samples will determine the quality of the audio
Quality is retained in transmission because only codes are transmitted
Audio can be recreated to the original quality by extracting the pattern from the digital code

## Slide 47: Sampling Factors
Sampling interval determined by sampling frequency
  Measured in Hz
Sampling depth
  Measured in bits
Sampling channels
  Mono or stereo, for example

## Slide 48: Sampling Example
CD quality audio
  44 KHz
  16 Bits
  Stereo

## Slide 49: Factors Affecting Quality
Number of bits used for binary encoding. Example: 4 bits allow 16 amplitude variations to be represented.
9 8 7 6 7 9
Sampling Interval

## Slide 50: Effect of Sampling Frequency
Higher sampling frequency
  Smaller sampling intervals
  Frequent sampling
  Better quality because the audio pattern is captured better
  Higher bandwidth required for transmission
  Higher disk space required for storage

## Slide 51: Computation of Bandwidth Requirement for Transmission
Problem:
  Compute the audio streaming rate for a voice grade circuit given that the number of bits used in the sampling is 8
Background information
  A voice grade circuit has a bandwidth of approximately 4000 Hz
General rule
  For acceptable quality, the audio must be sampled at twice the frequency of the voice grade bandwidth ….Nynguist Theorem

## Slide 52: Reason for Sampling at Twice the Frequency
Two peaks in each cycle
  Half of a cycle is above the datum line
  The other half of the cycle is below the datum line
Therefore, sample the audio at twice the frequency rate

## Slide 53: CD Sampling?
Sampling in this case is done for higher quality
  44 KHz
  16-bits
  Stereo

## Slide 54: Problem Representation
79 68 57 46 57 79
1/8000 Seconds (8000 HZ twice the frequency of the voice
grade circuit)
or 2X4000 samples per second
8 bits are used enabling
256 amplitudes to
represent the human
voice which is considered
to be adequate.

## Slide 55: Bandwidth Computation for Voice
Number of samples
  8000 per second
Number of bits per sample
  8
Bandwidth requirement
  8X8000 bps = 64,000 bps
  Approximately 64K bps
64K bps is the speed of a single ISDN (B) channel designed to carry voice

## Slide 56: Bandwidth of Voice Circuits
Generally speaking, the bandwidth requirement for uncompressed voice circuit is 64 Kbps
An example is the ISDN – B channel that was originally intended to carry voice
  Its bandwidth is 64 K bps

## Slide 57: Examples in Audio Quality and Bandwidth Requirement
CD quality
  44,100 Hz, 16 bit, Stereo
  1376K bps
Radio quality
  22,050 Hz, 8 bit, mono
  176K bps
Telephone quality
  11,025 Hz, 8bit, mono
  88K bps

## Slide 58: Recording Quality and Bandwidth Requirement Demonstration

## Slide 59: Recording Used in this Example
Settings for recording
  11K Hz, 8 bit and mono
Audio bandwidth requirement is 88K bps
Streaming is required to send the audio alone over the Internet
Approximate bandwidth required for both video and audio is 133K bps

## Slide 60: Audio Transmission In WWW
Client
Receive audio using
Internet Explorer
and a plug-in to receive
the audio stream.
Audio streaming requires compression.
Real-time audio
broadcast support
using streaming
server module.
28-56K bps
Web
Site

## Slide 61: Delivery of Instruction Over the WWW
Client
Web
Site
Receive audio/video using
Internet Explorer and Media
Player.
Audio/Video streaming.
Store streamed audio/
video using Windows Media.
28-56K bps

## Slide 62: Audio Files
Audio can be stored in different formats
  Uncompressed or raw file format (wav)
  Compressed format
  Streaming format
    Streamed audio is also compressed
    It is also designed for real-time delivery of audio

## Slide 63: Audio File Format
wav file format
  Basic file format in audio storage or raw file
rm file format
  Real audio’s streamed file format
  Streamed file
wma file format
  Microsoft’s audio streamed file format
  Streamed file
mp3 file format
  Compressed file
aac file format

## Slide 64: Quality Retention in Digital Transmission
Quality is retained in digital transmission because only the codes are transmitted
Quality is subject to some deterioration in analog transmission because the wave pattern is transmitted

## Slide 65: Analog Audio Transmission
Audio Prior
to Transmission
Audio with
Interference
Transmission
Audio After Filtering

## Slide 66: Passage of Analog Audio Over Analog Lines
Analog
Audio
Analog
Signals
Analog
Signals
Analog
Audio
Telephone
Telephone

## Slide 67: Recreation of Audio from Analog Signals
A difficult task
Complex algorithms are used to filter noise etc. for better audio transmission

## Slide 68: Signal Passage in Digital Audio Transmission
Encode
Transmit
Recreate
Decode
Audio
Audio

## Slide 69: A Sample Digital Audio Transmission Path
Analog
Audio
Digital
Audio
DSL
Modem
DSL
Modem
Digital
Audio
Analog
Audio
Sound
Card
Sound
Card
Digital
Network

## Slide 70: Sound Generation
Sound is recreated at destination
  Using FM synthesis
  Using wave table generation
Noise is not an issue in digital communication although it is an issue in digital transmission
  The reason, once again, is due to the fact that only codes are transmitted in digital transmission

## Slide 71: Digital Advantage in Audio Transmission
Only codes are transmitted
Original encoding is recreated
Original audio is reproduced
Again, sampling rate and number of bits used in each sample will determine the quality of audio transmitted

## Slide 72: Digitized Signal Transmission Over Analog Lines
Encode
Transmit
Recreate
Decode
Audio
Audio
Sampled Signals

## Slide 73: Sample Digital Audio Transmission Path Over Analog Lines
Analog
Audio
Digital
Audio
Modem
Modem
Digital
Audio
Analog
Audio
Sound
Card
Sound
Card
Analog
PSN

## Slide 74: Audio Transmission In WWW
Client
Web
Site
Receive audio using
Internet Explorer
and Windows Media Player.
Audio stream over analog/digital line.
Real-time audio
broadcast support
using Windows Media
streaming server module.

## Slide 75: Analog to Digital Converter
A to D and D to A converter
The chip that is responsible for this conversion is known as the DSP (Digital Signal Processor) chip
It is used in sound cards, modems etc. wherever there is a need for A to D and D to A conversion
The mass use of this chip in various devices has led to a drastic drop in the price of the chip and the devices

## Slide 76: Digital Signal Processor (DSP)
DSP
Digital
Analog

## Slide 77: Image Digitization
Image can be of the form black and white, gray scales, color
Factors that influence the digitization of image are as follows
  Resolution measured in pixels
  Color depth expressed in number of color variations

## Slide 78: Digitization Of Image: Overview
Pixel
Horizontal Resolution
Vertical Resolution

## Slide 79: Digitization of the Letter L
Number of bits
determine the
amount of
information that could
be stored.

## Slide 80: Digitization Of Image: The Process
Divide the image into a grid of pixels that may be considered as the sampling points of the image
Digitize information on each pixel
Store and transmit
Black and white 1 bit, gray color 15 bits and true color 24 bits(R,B,G) takes 8X4= 24

## Slide 81: Resolution
Horizontal resolution
  Number of horizontal pixels
Vertical resolution
  Number of vertical pixels
Image resolution
  Horizontal by vertical resolution
  Ex: 640 by 480

## Slide 82: Digitization of Black and White Image
White
  A pixel lit represents a 1
Black
  A pixel not lit represents a 0
Storage required per pixel
  1 bit
Storage required for 640 by 480 resolution image
  640 times 480 bits = 307,200 bits = 38.4K Bytes

## Slide 83: Digitization of Image Using Gray Scales
A pixel may take a value between 0 and 15 for 16 gray scales
A gray scale of 3 can be coded as 0011 and the others similarly using this 4 digit code
The bandwidth requirement for the transmission of a 640X480 image in this case is as follows:
  640X480X4 = 153.5K Bytes

## Slide 84: Digitization of Color Image
Image coding
  Each pixel may take a value between 0 and 255 if 256 colors are to be represented. i.e using 8 bits for each color
Storage requirement
  Digitizing of images requires substantial number of bytes and hence large storage space for processing
Bandwidth requirement
  Higher bandwidths are required to transmit color images

## Slide 85: Bandwidth Computation for Image with 256 Colors
Resolution is 640X480
8 bits are required to represent 256 colors
bandwidth requirement for the transmission of one image is as follows:
  640X480X8 = 307.2K Bytes

## Slide 86: The Effect of Color Depth and Resolution
Compare VGA, SVGA and XGA
  XGA provides the highest resolution
Practical implication
  More colors less resolution if bandwidth or storage is the limiting concern
  Example
    256 colors at lower resolution
    16 colors at higher resolution
Rule
  Higher the resolution the lower the number of colors available in general given the resource constraints such as bandwidth constraints

## Slide 87: Factors Affecting Bandwidth Requirement in Image Transmission
The higher the resolution, the higher the bandwidth requirement for transmission
The higher the color representation, also known as color depth, higher the bandwidth requirement
For true color, 24 (32) bits are required to represent each pixel
The file sizes in raw image capture can thus become very large

## Slide 88: Compression of Digitized Images
Compression is required to reduce the size of the image file
Large blocks of unchanged data in an image (background) offers an opportunity to compress the image
Image files are almost always compressed

## Slide 89: A Few Compression Formats
GIF
JPEG
MIC (Microsoft Image Composer)
PCD (KODAK) - Used by Corel
Uncompressed file exist in the form of bit mapped file with the extension of .BMP

## Slide 90: Image File Format Extensions
File formats often represent the compression procedure being used such as jpg representing the jpeg compression technique
Examples:
  Bmp – uncompressed file format
  Gif
  jpg
  pcd
  tiff
  pcx

## Slide 91: Loss-less Compression and Others
Some compression formats offer loss-free compression of the image
Others sacrifice minimal loss for the sake of reduced storage and bandwidth requirements
Fortunately, the loss is not easily detected by the naked eye

## Slide 92: Image Transmission Considerations
Sender
Receiver
Adjust image to suit available bandwidth.
Adjustable features are as follows.
- Resolution
- Color depth
Adjusting the size also reduces the bandwidth
requirement because of a corresponding reduction
in the number of pixels required to represent
the image.

## Slide 93: Modem Implication in Image Transmission
Modems also compress the data stream to achieve higher transmission speeds
Because of the fact that the images are already compressed, the full speed benefit may not be realized when images are transmitted over a modem connection
An already compressed image file does not, for instance, offer itself well to further compression in the modem

## Slide 94: Digitization of Video
Digitization of video is an extension of the process of digitizing an image
It amounts to the transmission of certain number of still images known as frames per second
Obviously, digitized video requires higher bandwidth for transmission and more space for storage

## Slide 95: Frame Rate
30 frames of images per second, in general, defines continuos motion
In communications, 25 frames per second is considered to be continuous motion
15 frames per second is currently used in video conferencing over digital lines for acceptable reception of video
It is also possible to engage in video conferencing at a frame rate of 5 frames per second

## Slide 96: Computation of Bandwidth for Raw Transmission of Video
Image resolution is 640X480
Number of colors is 256 (8 bit)
Acceptable reception requires 15 frames per second
Therefore, the bandwidth for the raw transmission is as follows:
  640X480X8X15 = 36.86M bps = 4.6M Bps

## Slide 97: Compression Standards Used in the Digitization of Video
MPEG 1, MPEG 2, MPEG 3 and MPEG 4
Windows Media Video
Real Media
Indio
QuickTime
ActiveMovie
AVI

## Slide 98: Streaming Formats for Video
Various streaming formats are supported by different vendors
  RealVideo
Microsoft’s streaming format
  wma (Windows Media Audio)
  wmv (Windows Media Video)
  Active Streaming Format (ASF)
Apple’s QuickTime format
Etc.

## Slide 99: Overview of Video Transmission in Video Conferencing
Minimum speed
  3 to 5 frames per second
Acceptable speed
  15 frames per second
Transmission techniques
  Data is compressed
  Only changes to the frame are transmitted

## Slide 100: Bandwidth Optimization in Video Conferencing
Minimize Windows for maximum efficiency
  Transmit less number of pixels in minimized form
Decrease the resolution
  Has the same effect as above
Decrease the number of colors displayed

## Slide 101: Communication Links for Video Conferencing
Possible on analog lines using 56,000 bps transmission speed but not desirable
Digital lines are preferred and the guidelines are as follows:
  Possible at 128k bps using ISDN lines
  Acceptable at 384k bps
  1M bps and above offer good quality video transmission

## Slide 102: ISDN Line Suitability
ISDN B channels can be assigned on a dynamic basis depending on the bandwidth requirement at any point in time during video conferencing

## Slide 103: Video Conferencing Products
Intel ProShare
CU-See Me
Picturetel
C-phone
etc.