## Slide 1: Overview
Transmission basics
  Terminology
    Signal
    Channel
    Electromagnetic spectrum
Two signal types
  Analog –vs- Digital
  Converting signals

## Slide 2: Terminology
Data – some entity that has meaning or conveys information
Signal – an electromagnetic representation of data
Transmission – moving data from source to destination through the use of signals

## Slide 3: Terminology
Communication channel – any pathway over which data are transmitted
  Can be a physical wire, radio wave, or any radiated source of energy (even if it has no physical presence)
  Transmitted data have a source and a destination

## Slide 4: Background
Electromagnetic radiation is the basis for all data transmission
Electromagnetic radiation propagates (spreads, disseminates) along different media (copper wire, fiber, etc.) and in free space (air)

## Slide 5: Background

## Slide 6: Background
Different parts of the electromagnetic frequency spectrum can be used for data transmission depending on
  The medium used
  The communications standards followed
The properties of the media being used affect
  Bandwidth, attenuation, noise, distortion

## Slide 7: Background
Bandwidth – range of frequencies occupied or used by a carrier wave
Attenuation – strength of signal decreases as it propagates
Noise – unwanted electromagnetic energy that degrades the signal (crosstalk, background interference)
Distortion – altering the original shape or characteristics of waveform

## Slide 8: Types of Signals: Analog & Digital
The two basic types of signals
  1) Analog
  2) Digital

## Slide 9: Analog Signals
Characterized by data whose value varies over a continuous range
  Temperature values at a certain location can assume an infinite number of values over time
Examples of analog data
  Video
  Audio
Historically telephony networks

## Slide 10: Digital Signals
Characterized by data whose value is limited to a finite set of values
Examples of digital data
  Text: printed English language (26 letters, 10 numbers, space, and punctuation)
  Morse code (binary example – either a dot or a dash)

## Slide 11: Types of signals
  Source: http://upload.wikimedia.org/wikipedia/commons/thumb/8/84/A-D-A_Flow.svg/981px-A-D-A_Flow.svg.png

## Slide 12: Analog versus digital
How does EMI impact each type of signal?

## Slide 13: Analog Signals
Analog signals can be represented by a waveform diagram
Electromagnetic waves have four properties that are all important with respect to transmitting signals
  1) Amplitude
  2) Frequency
  3) Wavelength
  4) Phase

## Slide 14: Electromagnetic Waveform Diagram

## Slide 15: Electromagnetic waveform
Amplitude – A measure of waveform strength at a given point in time
Amplitude at 0.25 sec = 5 volts
Amplitude at 0.5 sec = 0
Amplitude at 0.75 sec = -5 volts

## Slide 16: Electromagnetic waveform
Frequency - # of times a wave cycles from high amplitude to low amplitude and back again measured in cycles/sec (Hertz, Hz)
Frequency = 1 cycle / sec = 1 Hz
  1 MHz cable can transfer (106) or 1,000,000 wave cycles of current in 1 sec (wave peak to wave peak)
  100 MHz can transfer 100,000,000 wave cycles / sec

## Slide 17: Electromagnetic waveform
Wavelength – the distance between corresponding points on a wave cycle
Wavelength is generally expressed in some variant of meters or feet
Wavelength is inversely proportional to frequency - high frequency implies short wavelength

## Slide 18: Electromagnetic waveform
Phase – the progress of a wave over time in relationship to a fixed point
Example: two separate waves with same amplitude and frequency starting at different points in time
Phases are 90 degrees apart
Often hear phase difference or phase offset discussed

## Slide 19: Analog versus digital
Digital signals can be regenerated using repeaters and active hubs
  Cleaned up to prevent the accumulation of noise and distortion
  Allows signal to be transmitted over greater distances

## Slide 20: Analog versus digital
What happens to analog signals over distances even if they are amplified? Can you reconstruct the original signal?

## Slide 21: Analog versus digital
Analog: one-to-one relationship between how data are captured and recorded and how data are reproduced
  For example: microphone and speaker
    Capture sound as a stream of electrical fluctuations  pass through an amplifier  to speaker (no alteration)
Source: http://www.informit.com/library/content.aspx?b=Planet_Broadband&seqNum=14

## Slide 22: Analog versus digital
Digital: Reproduces text, pictures, sound, etc by sampling original output as high speed and assigning numeric code to represent the original (1s and 0s)
  Pass code through network to analog converter that turns code back into electrical fluctuations
Source: http://www.informit.com/library/content.aspx?b=Planet_Broadband&seqNum=14

## Slide 23: Clock Example
Analog clock – position of the hands on the clock corresponds to the time of day
Digital clock – the time of day is represented as a discrete set of numeric values
Based on SP Bali (2005), “2000 Solved Problems in Digital Electronics”

## Slide 24: Analog to digital conversion

## Slide 25: Data / signal combinations
Digital signals represent data with sequence of voltage pulses
  Digital data / digital signal
  Analog data / digital signal
Analog signals represent data with continuously varying electromagnetic wave
  Digital data / analog signal
  Analog data / analog signal
  Source: Tseng, http://www.cs.sunysb.edu/~jgao/CSE370-spring06/lecture2.pdf

## Slide 26: Data / signal combinations
Different types of data may be digital or analog by nature
Different types of networks use different types of signals
  A wired LAN using Ethernet uses baseband, digital signaling
  A WiFi LAN uses broadband, analog signaling
Potential benefits and drawbacks associated with different types of signals

## Slide 27: Analog to digital conversion
Convert commonly occurring analog data / information such as voice and video to digital data for transmission over a either analog/digital network
We can transmit digital data
  Faster
  Cheaper
  With fewer errors

## Slide 28: Advantages of Digital Signals
Digital circuits have only two states so:
  Changes in value have little effect on digital signals
  Noise and other forms of interference have little effect on digital signals
  Little chance of error because voltage in a digital circuit must be in one state or the other
  Information storage is easy
Based on SP Bali (2005), “2000 Solved Problems in Digital Electronics”

## Slide 29: Advantages of Digital Signals
  Operation can be readily programed
  Can fabricate more digital circuitry onto integrated circuits
Based on SP Bali (2005), “2000 Solved Problems in Digital Electronics”

## Slide 30: Disadvantages of Digital Signals
The ONE major disadvantage is that the real-world is analog in nature
When dealing with analog inputs and outputs you will always have to: 1) convert analog to digital (ADC), 2) process the digital data, 3) convert the digital data back to analog output (DAC)
Based on SP Bali (2005), “2000 Solved Problems in Digital Electronics”

## Slide 31: Digital Networks
Digital transmission enables networks to support many services
E-mail
Telephone
TV

## Slide 32: Questions of Interest
How long will it take to transmit a message?
  How many bits are in the message (text, image)?
  How fast does the network/system transfer information?
Can a network/system handle a voice (video) call?
  How many bits/second does voice/video require? At what quality?
How long will it take to transmit a message without errors?
  How are errors introduced?
  How are errors detected and corrected?
What transmission speed is possible over radio, copper cables, fiber, infrared, …?

## Slide 33: Data Representation-Bits, numbers, information
Bit: number with value 0 or 1
  n bits: digital representation for 0, 1, … , 2n
  Byte or Octet, n = 8
  Computer word, n = 16, 32, or 64
n bits allows enumeration of 2n possibilities
  n-bit field in a header
  n-bit representation of a voice sample
  Message consisting of n bits
The number of bits required to represent a message is a measure of its information content
  More bits → More content

## Slide 34: Block vs. Stream Information
Block
Information that occurs in a single block
  Text message
  Data file
  JPEG image
  MPEG file
Size = bits / block
or bytes/block
  1 Kbyte = 210 bytes
  1 Mbyte = 220 bytes
  1 Gbyte = 230 bytes
Stream
Information that is produced & transmitted continuously
  Real-time voice
  Streaming video
Bit rate = bits / second
  1 Kbps = 103 bps
  1 Mbps = 106 bps
  1 Gbps = 109 bps

## Slide 35: Transmission Delay
What can be done to reduce the delay?
Use data compression to reduce L
Use higher-speed modem to increase R
Place server closer to reduce d
L number of bits in message
R bps speed of digital transmission system
L/R time to transmit the information
d distance in meters
c speed of light (3x108 m/s in vacuum)
tprop time for signal to propagate across medium
Delay = tprop + L/R = d/c + L/R seconds

## Slide 36: Compression
Information usually not represented efficiently
Data compression algorithms
  Represent the information using fewer bits
  Noiseless: original information recovered exactly
    e.g., zip, compress, GIF, fax
  Noisy: recover information approximately
    JPEG
    Tradeoff: # bits vs. quality
Compression Ratio
  #bits (original file) / #bits (compressed file)

## Slide 37: Color Image
H
W
=
+
+
H
W
H
W
H
W
Color image
Red component image
Green component image
Blue component image
Total bits = 3  H  W pixels  B bits/pixel = 3HWB bits
Example: 810 inch picture at 400  400 pixels per inch2
400  400  8  10 = 12.8 million pixels
8 bits/pixel/color
12.8 megapixels  3 bytes/pixel = 38.4 megabytes

## Slide 38: Examples of Block Information
Type | Method | Format | Original | Compressed(Ratio)
Text | Zip, compress | ASCII | Kbytes- Mbytes | (2-6)
Fax | CCITT Group 3 | A4 page 200x100 pixels/in2 | 256 Kbytes | 5-54 Kbytes (5-50)
Color Image | JPEG | 8x10 in2 photo 4002 pixels/in2 | 38.4 Mbytes | 1-8 Mbytes (5-30)

## Slide 39: Stream Information
Th e s p ee ch s i g n al l e v el v a r ie s w i th t i m(e)
A real-time voice signal must be digitized & transmitted as it is produced
Analog signal level varies continuously in time

## Slide 40: Digitization of Analog Signal
Sample analog signal in time and amplitude
Find closest approximation
D/2
3D/2
5D/2
7D/2
-D/2
-3D/2
-5D/2
-7D/2
Original signal
Sample value
Approximation
Rs = Bit rate = # bits/sample x # samples/second
3 bits / sample

## Slide 41: Bit Rate of Digitized Signal
Bandwidth Ws Hertz: how fast the signal changes
  Higher bandwidth → more frequent samples
  Minimum sampling rate = 2 x Ws
Representation accuracy: range of approximation error
  Higher accuracy
  → smaller spacing between approximation values
  → more bits per sample

## Slide 42: Example: Voice & Audio
Telephone voice
Ws = 4 kHz → 8000 samples/sec
8 bits/sample
Rs=8 x 8000 = 64 kbps
Cellular phones use more powerful compression algorithms: 8-12 kbps
CD Audio
Ws = 22 kHz → 44000 samples/sec
16 bits/sample
Rs=16 x 44000= 704 kbps per audio channel
MP3 uses more powerful compression algorithms: 50 kbps per audio channel

## Slide 43: Video Signal
Sequence of picture frames
  Each picture digitized & compressed
Frame repetition rate
  10-30-60 frames/second depending on quality
Frame resolution
  Small frames for videoconferencing
  Standard frames for conventional broadcast TV
  HDTV frames
30 fps
Rate = M bits/pixel x (W x H) pixels/frame x F frames/second

## Slide 44: Video Frames
Broadcast TV
at 30 frames/sec =
10.4 x 106 pixels/sec
720
480
HDTV
at 30 frames/sec =
67 x 106 pixels/sec
1080
1920
QCIF videoconferencing
(144 lines and 176 pixels per line )
at 30 frames/sec =
760,000 pixels/sec
144
176

## Slide 45: Digital Video Signals
Type | Method | Format | Original | Compressed
Video Confer-ence | H.261 | 176x144 or 352x288 pix @10-30 fr/sec | 2-36 Mbps | 64-1544 kbps
Full Motion | MPEG2 | 720x480 pix @30 fr/sec | 249 Mbps | 2-6 Mbps
HDTV | MPEG2 | 1920x1080 pix @30 fr/sec | 1.6 Gbps | 19-38 Mbps

## Slide 46: Transmission of Stream Information
Constant bit-rate
  Signals such as digitized telephone voice produce a steady stream: e.g., 64 kbps
  Network must support steady transfer of signal, e.g., 64 kbps circuit
Variable bit-rate
  Signals such as digitized video produce a stream that varies in bit rate, e.g., according to motion and detail in a scene
  Network must support variable transfer rate of signal, e.g., packet switching or rate-smoothing with constant bit-rate circuit

## Slide 47: Stream Service Quality Issues
Network Transmission Impairments
  Delay: Is information delivered in timely fashion?
  Jitter: Is information delivered in sufficiently smooth fashion?
  Loss: Is information delivered without loss? If loss occurs, is delivered signal quality acceptable?
Applications & application layer protocols developed to deal with these impairments

## Slide 48: A Transmission System
Transmitter
Converts information into signal suitable for transmission
Injects energy into communications medium or channel
  Telephone converts voice into electric current
  Modem converts bits into tones
Receiver
Receives energy from medium
Converts received signal into form suitable for delivery to user
  Telephone converts current into voice
  Modem converts tones into bits
Receiver
Communication channel
Transmitter

## Slide 49: Transmission Impairments
Communication Channel
Pair of copper wires
Coaxial cable
Radio
Light in optical fiber
Light in air
Infrared
Transmission Impairments
Signal attenuation
Signal distortion
Spurious noise
Interference from other signals
Transmitted Signal
Received Signal
Receiver
Communication channel
Transmitter

## Slide 50: Analog Long-Distance Communications
Each repeater attempts to restore analog signal to its original form
Restoration is imperfect
  Distortion is not completely eliminated
  Noise & interference is only partially removed
Signal quality decreases with # of repeaters
Communications is distance-limited
Still used in analog cable TV systems
Analogy: Copy a song using a cassette recorder
Source
Destination
Repeater
Transmission segment
Repeater
. . .

## Slide 51: Analog vs. Digital Transmission
Analog transmission: all details must be reproduced accurately
Sent
Sent
Received
Received
Distortion
Attenuation
Digital transmission: only discrete levels need to be reproduced
Distortion
Attenuation
Simple Receiver: Was original pulse positive or negative?

## Slide 52: Digital Long-Distance Communications
Regenerator recovers original data sequence and retransmits on next segment
Can design it so error probability is very small
Then each regeneration is like the first time!
Analogy: copy an MP3 file
Communications is possible over very long distances
Digital systems vs. analog systems
  Less power, longer distances, lower system cost
  Monitoring, multiplexing, coding, encryption, protocols…
Source
Destination
Regenerator
Transmission segment
Regenerator
. . .

## Slide 53: Digital Binary Signal
For a given communications medium:
How do we increase transmission speed?
How do we achieve reliable communications?
Are there limits to speed and reliability?
+A
-A
0
T
2T
3T
4T
5T
6T
1
1
1
1
0
0
Bit rate = 1 bit / T seconds

## Slide 54: Pulse Transmission Rate
Objective: Maximize pulse rate through a channel, that is, make T as small as possible
Channel
t
t
If input is a narrow pulse, then typical output is a spread-out pulse with ringing
Question: How frequently can these pulses be transmitted without interfering with each other?
Answer: 2 x Wc pulses/second
where Wc is the bandwidth of the channel
T

## Slide 55: Multilevel Pulse Transmission
Assume channel of bandwidth Wc, and transmit 2 Wc pulses/sec (without interference)
If pulses amplitudes are either -A or +A, then each pulse conveys 1 bit, so
Bit Rate = 1 bit/pulse x 2Wc pulses/sec = 2Wc bps
If amplitudes are from {-A, -A/3, +A/3, +A}, then bit rate is 2 x 2Wc bps
By going to M = 2m amplitude levels, we achieve
Bit Rate = m bits/pulse x 2Wc pulses/sec = 2mWc bps
In the absence of noise, the bit rate can be increased without limit by increasing m

## Slide 56: Noise & Reliable Communications
All physical systems have noise
  Electrons always vibrate at non-zero temperature
  Motion of electrons induces noise
Presence of noise limits accuracy of measurement of received signal amplitude
Errors occur if signal separation is comparable to noise level
Bit Error Rate (BER) increases with decreasing signal-to-noise ratio
Noise places a limit on how many amplitude levels can be used in pulse transmission

## Slide 57: Signal-to-Noise Ratio
SNR =
Average signal power
Average noise power
SNR (dB) = 10 log10 SNR
Signal
Noise
Signal + noise
Signal
Noise
Signal + noise
High
SNR
Low
SNR
t
t
t
t
t
t
error
No errors

## Slide 58: Shannon Channel Capacity
Arbitrarily reliable communications is possible if the transmission rate R < C.
If R > C, then arbitrarily reliable communications is not possible.
“Arbitrarily reliable” means the BER can be made arbitrarily small through sufficiently complex coding.
C can be used as a measure of how close a system design is to the best achievable performance.
Bandwidth Wc & SNR determine C
C = Wc log2 (1 + SNR) bps

## Slide 59: Example
Find the Shannon channel capacity for a telephone channel with Wc = 3400 Hz and SNR = 10000
C = 3400 log2 (1 + 10000)
= 3400 log10 (10001)/log102 = 45200 bps
Note that SNR = 10000 corresponds to
SNR (dB) = 10 log10(10001) = 40 dB

## Slide 60: Bit Rates of Digital Transmission Systems
System | Bit Rate | Observations
Telephone twisted pair | 33.6-56 kbps | 4 kHz telephone channel
Ethernet twisted pair | 10 Mbps, 100 Mbps, 1 Gbps | 100 meters of unshielded twisted copper wire pair
Cable modem | 500 kbps-4 Mbps | Shared CATV return channel
ADSL | 64-640 kbps in, 1.536-6.144 Mbps out | Coexists with analog telephone signal
2.4 GHz radio | 2-11 Mbps | IEEE 802.11 wireless LAN
28 GHz radio | 1.5-45 Mbps | 5 km multipoint radio
Optical fiber | 2.5-10 Gbps | 1 wavelength
Optical fiber | >1600 Gbps | Many wavelengths

## Slide 61: Examples of Channels
Channel | Bandwidth | Bit Rates
Telephone voice channel | 3 kHz | 33 kbps
Copper pair | 1 MHz | 1-6 Mbps
Coaxial cable | 500 MHz (6 MHz channels) | 30 Mbps/ channel
5 GHz radio (IEEE 802.11) | 300 MHz (11 channels) | 54 Mbps / channel
Optical fiber | Many TeraHertz | 40 Gbps / wavelength